## Slide 1: Facilitating Research on the NVIDIA Grace Hopper Superchip: The CU Boulder Research Computing Experience

## Slide 2: Facilitating Research on the NVIDIA Grace Hopper Superchip: The CU Boulder Research Computing Experience
Presenter: Brandon Reyes
Website: www.rc.colorado.edu
Helpdesk: rc-help@colorado.edu
Slides: https://github.com/ResearchComputing/rmacc_2025

## Slide 3: Session Overview
GH200 architecture overview
GH200 software stack
Beta testing phase
Successful use cases
Potential future directions
How can you run on the GH200s?

## Slide 4: GH200 architecture overview
The Grace Hopper Superchip (GH200) is a newer chip provided by NVIDIA. Its unique architecture allows the GPU and CPU to efficiently share and exchange memory.
Image provided by https://resources.nvidia.com/en-us-grace-cpu/nvidia-grace-hopper
Ideal for workloads that utilize the CPU and GPU to a high degree
Although powerful, the Arm-based CPU can present support challenges
  HPC systems often have software built only for x86_64 architectures
  Utilizing the full capabilities can require CUDA code changes

## Slide 5: Specifications for our 2 GH200 nodes
Grace CPU has 72 cores and roughly 480 GB of RAM
  Arm based (Neoverse V2)
Hopper GPU has roughly 100 GB of VRAM
CPU and GPU are connected via NVIDIA NVLink-C2C
  This enables efficient and seamless memory transfer between the two components
FAST I/O speed (512 GB/s)
  Top I/O speeds only apply to the SSD
Roughly 1.7 TB of usable SSD on the node

## Slide 6: GH200 software stack
Due to the unique architecture and Arm-based processors, we opted for a curated and paired-down software stack.
CUDA compilers through NVIDIA HPC SDK e.g. nvcc, nvc++
CUDNN libraries
Miniforge (mamba and conda)
  We found that most libraries that provided an aarch64 version (with GPU capabilities) worked on the GH200s
Apptainer
  A large selection of compatible containers are available through NVIDIA’s NGC catalog

## Slide 7: Beta testing phase
Goal: to identify any issues associated with the GH200s, software requirements, and workflows that could take advantage of the architecture
Directed towards users with established GPU workflows
An initial consultation was held to determine if their existing GPU workflows met the following criteria:
  Peak GPU usage was roughly half the size of the VRAM
  Peak CPU utilization was at least 70%
    Exceptions were made for applications that required the large amount of available RAM
  Software utilized was available for the GH200s

## Slide 8: Beta testing phase cont.
Once approved, we
Installed all necessary software and ran a trimmed-down version of the user’s code
Added users to the provided reservation
  Enabled us to use established QoS and provide access only to approved users
Created an allocation specific to the user
  Facilitated easier analysis of hardware usage
Onboarded the user to the node
  Provided them information on how to run on the node and how to install their own software
Provided hands-on support for any issues encountered

## Slide 9: Successful use cases
All users in the beta testing phase reported that they would not be able to run their workflows without the GH200s!
All user workflows were AI based:
  CNNs, LSTMs, KANs, MLPs
  Gradient boosted trees (XGBoost)
  Image segmentation (SAM2)
Training large models and hyperparameter tuning
  We have seen at least 2X speedup, some users reported 10X speedup
Inference for Large Language Models
  We were able to run Llama 3.1 405b (requires ~300 GB of memory)

## Slide 10: Potential future directions
Moving out of the beta testing phase:
  Node access will be provided via a QoS
  Job submissions will be limited to 1 per user
  Workflows will continue to be evaluated before permission is granted
    Ensures proper node use and well-informed users
We are considering utilizing Multi-Instance GPU (MIG) on one of the nodes
  MIG would provide more resources for prototyping and testing purposes
  We found that some users could continue to benefit from the GH200 architecture, even if they had half the GPU resources

## Slide 11: How can you run on the GH200s?
Submit a ticket to rc-help@colorado.edu
In the subject provide: I am interested in running “X application” on the GH200s
In the email body:
  Short description of what your workflow does
  Why you believe the GH200s would be beneficial to your workflow
  Provide us with Linux paths to the code you would like to run
  If possible, any JobIDs of this workflow you have ran on a GPU node

## Slide 12
Slides: https://github.com/ResearchComputing/rmacc_2025
Thank you!