## Slide 1: Deploying and Utilizing the NVIDIA Grace Hopper Superchip: The CU Boulder Research Computing Experience

## Slide 2: Deploying and Utilizing the NVIDIA Grace Hopper Superchip: The CU Boulder Research Computing Experience
Presenter: Brandon Reyes
Website: www.rc.colorado.edu
Helpdesk: rc-help@colorado.edu
Slides: https://github.com/ResearchComputing/rmacc_2025

## Slide 3: Session Overview
GH200 architecture overview
GH200 software stack
Beta testing phase
Successful use cases
Potential future directions
How can you run on the GH200s?

## Slide 4: GH200 architecture overview
The Grace Hopper Superchip (GH200) is a newer chip provided by NVIDIA. Its unique architecture allows the GPU and CPU to efficiently share and exchange memory.
Image provided by https://resources.nvidia.com/en-us-grace-cpu/nvidia-grace-hopper

## Slide 5: Specifications for our 2 GH200 nodes
Grace CPU has 72 cores and roughly 480 GB of RAM
  Arm based (Neoverse V2)
Hopper GPU has roughly 100 GB of VRAM
CPU and GPU are connected via NVIDIA NVLink-C2C
  This enables efficient and seamless memory transfer between the two components
FAST I/O speed (512 GB/s)
  Top I/O speeds only apply to the SSD
Roughly 1.7 TB of usable SSD on the node

## Slide 6: GH200 software stack
Due to the unique architecture, we opted for a curated software stack. We currently provide:
CUDA compilers through NVIDIA HPC SDK e.g. nvcc, nvc++
CUDNN libraries
Miniforge (mamba and conda)
  We found that most libraries that provided an aarch64 version (with GPU capabilities) worked on the GH200s
Apptainer
  A large selection of compatible containers are available through NVIDIA’s NGC catalog

## Slide 7: Beta testing phase
Goal: to identify any issues associated with the GH200s, software requirements, and workflows that could take advantage of the architecture
Directed towards users with established GPU workflows
An initial consultation was held to determine if the workflow was appropriate for the GH200s
Once approved:
  User support would install all necessary software
  Users were provided a reservation and allocation for the nodes
  A detailed onboarding consultation was held
  User support provided hands-on support for any issues encountered

## Slide 8: Successful use cases
All users in the beta testing phase reported that they would not be able to run their workflows without the GH200s
All user workflows were AI based:
  CNNs, LSTMs, KANs, MLPs
  Gradient boosted trees (XGBoost)
  Image segmentation (SAM2)
Training large models and hyperparameter tuning
  We have seen at least 2X speedup, some users reported 10X speedup
Inference for Large Language Models
  We were able to run Llama 3.1 405b (requires ~300 GB of memory)

## Slide 9: Potential future directions
Currently moving out of the beta testing phase
  Will not open the GH200s systemwide, but will have a QoS that users will be added to
  We will continue to evaluate workflows before granting permission to these nodes
    Ensures that the nodes are being properly used
    Ensures that users understand the difference in architecture
  Preference will be given to users who need the hardware
Given our constraint of 2 nodes, we are considering utilizing Multi-Instance GPU (MIG) to split the GPU in half on one of the nodes.
  Allows quick access to resources for prototyping and testing purposes
  We found that most users would continue to benefit from the GH200 architecture, even if they had half the GPU resources.

## Slide 10: How can you run on the GH200s?
Submit a ticket to rc-help@colorado.edu
  In subject include:
    You are interested in running “X application” on the GH200s
  In the email body:
    Short description of what your workflow does
    Why you believe the GH200s would be beneficial to your workflow
    Provide us with Linux paths to the code you would like to run
    If possible, any JobIDs of this workflow you have ran on a GPU node

## Slide 11
Slides: https://github.com/ResearchComputing/rmacc_2025
Thank you!